90 DEGREE QUICK CONNECT ELBOW

Task Force Tips model #AF9QNR-SP-01 90 degree quick connect elbow shall be provided. For corrosion resistance, the elbow shall be constructed of hardcoat anodized aluminum alloy, have a silver powder coat finish inside and out and include a polymer bearing ring for prevention of galvanic corrosion. The quick connect shall be capable of attachment to Task Force Tips 4” female NPT inlet adapter, 4” ANSI 150 flange inlet adapter or VUM Valve Under Monitor with quick connect outlet.

The unit shall have a large carrying handle, a boss for drilling and threading for installation of a drain/bleeder or pressure gauge. The elbow shall meet a 900 PSI hydrostatic test and comply with the current NFPA 1965 Standard. The unit shall be covered by a five-year warranty.

The elbow shall be configured with a 4-1/2" female NH swivel long handle coupling with 3-1/2” additional height with proprietary alignment tab and a 4" Storz rigid connection.