1250 GPM FIXED LOCATION MONITOR

Task Force Tips Monsoon, model # Y4-TP5A-Z manually controlled monitor shall be provided. The monitor shall operate with a hand wheel which controls a stainless steel worm gear for elevation adjustment and a long tiller bar for rotation adjustment and include a locking knob.

The monitor shall have the following capabilities:

Full horizontal rotation with continuous 360 degree travel;

135 degrees of vertical travel from 45 degrees below and 90 degrees above horizontal;

Field changeable elevation stops at 30 and 45 degrees above horizontal and 30 degrees below horizontal;

Field changeable rotation stops shall be provided at 45, 90 and 135 degrees left and/or right of center;

Flow capability of 1250 GPM with a friction loss of no more than 6 psi;

Maximum operating pressure of 200 PSI.

For resistance to corrosion the monitor shall be constructed from hardcoat anodized aluminum with an American red powder coat interior and exterior finish. A threaded port for an optional pressure gauge shall be provided. The unit shall have a unique serial number and be covered by a five-year warranty.

The monitor shall be designed with a unique waterway that minimizes the path of travel, reduces friction loss and turbulence, and produces a far reaching water stream. The monitor shall be configured with a Task Force Tips code RPF threaded inlet to mate with Task Force Tips Extend-A-Gun RC4 telescoping waterway and 2-1/2" male NH outlet. The unit shall be covered by a five-year warranty.